PRODUCT SPECIFICATION SHEET

MAXIMA ELLIPSE TISSUE DISPENSER

KHP PART No: TSD MAX ELP

###### DESCRIPTION

- Accepts range of readily available jumbo toilet rolls up to (260mm max.

- Replaceable front insert

- Part used roll (135mm max.

- Accepts core diameters 56mm – 62mm

- Roll held on braked mandrel, giving smooth controlled operation

- Cutting teeth around bottom edges assist tearing of paper.

- Dispenser can be sited on left or right hand side of cubical.

- Dampened opening of hinged cover.

- Lock acts on 2 independent catches for added security and reliability.

- Tray prevents premature use of full roll.

- Tray returns to start position automatically when cover is opened.

###### DIMENSIONS

MATERIALS

Constructed mainly from ABS, as well as other engineering thermoplastics, such as Acetal and Polypropylene. Dispenser can be recycled or disposed of in accordance with local regulations.

PACKING

Individual units packed in polybags with cardboard dividers in between them.

Individual weight: 1.55kgs

4 units packed into carton: 560x430x300mm

Total weight: 7kgs approximately